RTOS Concepts
&
RTAI
Sowjanya
C-DAC, Hyderabad

---
Agenda
- Real Time Systems
- RTOS Vs GPOS
- RTOS Services
- Real Time Linux Variants
- Real Time Application Interface(RTAI)

---
Real Time Systems
Typical real-time control system including inputs from sensors and imaging devices and producing control signals and display information.

---
Real Time Systems
- Correctness
  - The correctness of the system depends not only on the logical result, but also on the time at which the results are produced.
- Predictability
  - Possible to show at “design time” that all the timing constraints of the application will be met.
- Deterministic
  - For each possible state and each set of inputs, a unique set of outputs and next state of the system can be determined.

---
Real Time Systems
- Classification of RT systems
  - Soft real-time system
    - Performance is degraded but not destroyed by failure to meet response-time constraints.
    - Eg: Mutlimedia, Interactive video games
  - Firm real-time system
    - Missing more than few deadlines, may lead to catastrophe
    - Eg: Robot weed killer
  - Hard real-time system
    - Failure to meet a single deadline may lead to catastrophic failure
    - Eg: Aircraft Control Systems, Nuclear Power Stations, Chemical Plants, Life support systems

---
Real Time Systems Performance
- Predictability
  - Possible to show at “design time” that all the timing constraints of the application will be met.
    - For static systems, 100% guarantee
    - For dynamic systems, 100% guarantee cannot be given since the characteristics of tasks are not known a priori.
    - In dynamic systems, once a task is admitted into the system, its guarantee should never be violated, as long as conditions hold.
- Deterministic
  - For each possible state and each set of inputs, a unique set of outputs and next state of the system can be determined.

---
Real Time Tasks
- Periodic tasks
  - Time-driven, characteristics are known a priori (pi, ci)
  - Eg: Task monitoring temperature of a patient in an ICU
- Aperiodic tasks
  - Event-driven, characteristics not known a priori (ai, ri, ci, di)
  - Task activated on detecting change in patient’s condition
- Sporadic Tasks
  - Aperiodic tasks with known minimum inter-arrival time.
   pi : task period  ai : arrival time ri : ready time di : deadline ci : worst case exec time

---
Real Time Tasks
- The CPU utilization or time-loading factor, is a measure of the percentage of non-idle processing
  - Utilization factor ui for a Task ti is (ci /pi )
  - Overall system utilization (U) = ∑ ui

---
RTOS Vs GPOS
#	Metric of Evaluation	General Purpose OS	Real Time OS
1	Determinism	Non Deterministic	Deterministic – Kernel functions should execute in a fixed amount of time
2	Load Independent Timing	Not Applicable – Response becomes sluggish as number of tasks increase	Remains Constant – Generally Priority based execution. Time Slices are available only among tasks that hold the same priority
3	Task Level Scheduling	Generally Round Robin Scheduling, Sometimes Priority based scheduling – Efforts are made to ensure that all tasks get a chance to execute	Priority based Preemptive Scheduling – Ensure that the Highest Priority task is always executed, even if it is the most frequent
4	Interrupt Management	Nesting may be disabled. Interrupt latency, response and recovery are not performance metrics	Nesting is always enabled. Interrupt latency, response and recovery are very important performace metrics

---
RTOS Architecture
An RTOS consists of
Kernel (micro-kernel)
Device Manager
Networking protocol s/w
Libraries
File sys (optional)
comm sw
device mgr
file sys
kernel
libraries
Operating system
Application Programming i/f
Application s/w

---
RTOS Services
- Multi-tasking, Task & Thread Management
  - Creation and scheduling of tasks.
  - Priority based pre-emptive scheduling
- Inter Task Synchronization and Inter Task Communications through mutual exclusions, signals, messages, shared memory, etc
- Usually no Memory Management
- Timer Services such as periodic and aperiodic interrupts

---
RTOS Services
- Device drivers to service the needed special devices
- Communication Protocol software (networking through ethernet, wireless, etc)
- Application Programming Interface (APIs) to access kernel Services

---
Kernel Types – Non Preemptive Kernel
low priority task
1
2
ISR
ISR makes the high priority task ready
3
4
5
6
high priority task

---
Kernel Types – Preemptive Kernel
low priority task
1
2
ISR
3
high priority task
4

---
Task States
Waiting
Ready
Running
ISR
Dormant

---
Interrupts
- When an interrupt occurs,
  - CPU saves its context on the stack, Jumps to the Interrupt Servicing Routine (ISR), Executes ISR and Returns
  - Interrupt Latency
    - max time interrupts are disabled + time to begin servicing the interrupt
  - Interrupt Response Time
    - Interrupt Latency + time to start execution of 1st instruction in ISR
  - Interrupt Recovery Time
    - time for CPU to return to interrupted code / highest priority task

---
Interrupts in Non Preemptive Kernels
Interrupt
Request
CS
ISR
IL
IRec
IR
Time ->
Background Process
CPU Context Saved
User Code ISR

---
Interrupts in a preemptive kernel
Background Process
CPU Context Saved
User Code ISR
Time ->
ISR
Interrupt
Request
IL
IR
CS
IRec2
Preemptive Kernel
Entry
Exit
IRec1
ISR

---
Priority Inversion, Inheritance and Ceiling
Task HP
Task MP
Task LP
Shared Resource

---
Overview of available RTOS’s
Three categories of real-time operating systems:
Small, proprietary kernels. e.g. VRTX32, pSOS, VxWorks, Windows CE, MicroC-OS/III*
Real-time Linux extensions: RT-Linux, Xenomai, RTAI
Research kernels: MARS, ARTS, Spring, Polis, MicroC-OS/II
Hard
Real Time Operating System
Vx Works, Lynx, QNX
Intime, HyperKernel, RTX
Windows CE
General Purpose Operating System
Linux, NT
Soft
RT Systems & RTOS

---
Variants of Real-Time Linux
- Two primary variants of hard real-time Linux available are RTLinux and RTAI.
  - Real Time Linux (RTLinux) was developed at the New Mexico Institute of Technology
    - www.rtlinux.org
  - Real-Time Application Interface (RTAI) was developed by programmers at the Department of Aerospace Engineering, Milano
    - www.aero.polimi.it/~rtai

---
Real Time Linux

---
The Real-Time Linux
- In a real-time Linux system
  - Real-time linux scheduler treats Linux kernel as the idle task
    - Linux only executes when there are no real time tasks to run, and when the real time kernel is inactive.
  - Linux is not permitted to disable hardware interrupts, I.e cannot add latency to the interrupt response time
    - When Linux code tries to disable interrupts, the real time system intercepts the request, records it. Doesn't actually disable ITRs
  - When an interrupt occurs, the real time kernel intercepts the interrupt and dispatches
    - First real time handlers are invoked then Linux handlers

---
The Real-Time Linux
- Real time kernel never waits for the Linux side to release any resources.
  - Communication links that are used to transfer data between real time tasks and Linux processes are non-blocking on the real time side.
- Linux operating system does as much as is practicable
  - System and Device initialization
  - Blocking dynamic resource allocation
  - Thread of execution that can be blocked
  - Loadable module mechanism to install components of the Real-Time system.

---
The Real-Time Linux
- The Real Time kernel, all its component parts, and the real time applications run in Linux kernel address space as kernel modules.
  - Advantage: Aids in modularity
  - Disadvantage: A bug in a real time task can crash the whole system.
- Real-time Linux decouples the services of the real time kernel from the services of the general purpose Linux kernel.
  - Real-time kernel can be kept small and simple, each service can be optimized independently

---
RTLinux and RTAI
- In both RTLinux and RTAI, all interrupts are initially handled by the real time kernel and are passed to Linux only when there are no active real time tasks.
  - When Linux has disabled interrupts, a emulation software will queue interrupts that have been passed on by the real time kernel.
  - All the occurrences of cli, sti, and iret in the Linux source are replaced with emulating macros.

---
Real-Time Application Interface (RTAI)‏
- RTAI versions over 3.0 use an Adeos kernel patch, comprising an Interrupt Pipeline, where different Operating System Domains register interrupt handlers.
  - RTAI transparently takes over interrupts while leaving the processing of all others to Linux.
  - Use of Adeos also frees RTAI from patent restrictions caused by RTLinux project.
    Note: Adeos was developed in the context of RTAI to separate the HAL from the real-time kernel.

---
Real-Time Application Interface (RTAI)‏‏
- RTAI versions over 3.0 use an Adeos kernel patch, comprising an Interrupt Pipeline, where different Operating System Domains register interrupt handlers.
- Adeos (Adaptive Domain Environment for Operating Systems) is a nanokernel hardware abstraction layer (HAL) that operates between computer hardware and the operating system that runs on it.
  - Provides environment for sharing hardware resources among multiple OS, or multiple instances of a single OS

---
Real-Time Application Interface (RTAI)‏
- RTAI provides deterministic and preemptive performance in addition to allowing the use of all standard Linux drivers, applications and functions.
- RTAI's feactures:
  - Traditional RTOS IPCs including: Semaphores, mailboxes, FIFOs, shared memory, and RPCs
  - POSIX 1003.1c (Pthreads, mutexes and condition variables)‏ & POSIX 1003.1b (Pqueues only)‏ compatibility

---
Real-Time Application Interface (RTAI)‏
- RTAI's feactures:
  - /proc interface – which provides information on the real-time tasks, modules, services and processes extending the standard Linux /proc file-system support.
  - LXRT – which allows the use of the RTAI system calls from within standard user space
  - UniProcessor, Multi-UniProcessor and Symmetric Multi- processor (SMP) support
  - One-shot and periodic schedulers

---
RTAI Performance
- RTAI's performance is very competitive with the best commercial Real Time Operating Systems (such as VxWorks, QNX etc)‏
- Offers:
  - Context switch time: 4 uSec
  - Interrupt response: 20 uSec
  - 100 KHz periodic tasks
  - 30 KHz one-shot task rate

---
RTAI Components
- The three main RTAI components are:
  - The Interrupt Dispatcher
  - The Scheduler
  - The FIFO

---
RTAI Interrupt Dispatcher
- The dispatcher is a handler called via the IDT when interrupts occur.
  - Activates the right handler depending on the owner of the driver: RTAI, Linux or both (RTAI first then Linux).
  - The addresses of the Linux handlers are saved before changing the IDT in the HAL.
  - Takes into account the “SRQ(service request) handlers”.
    - SRQ is a handler used for a system call implementation. SRQ can be either RTAI handler (e.g.: fifo) or User handler.
  - RTAI manages up to 31 SRQ's. SRQ handler addresses are stored in IDT.

---
RTAI Interrupt Dispatcher

---
RTAI Scheduler
- The scheduler is in charge of distributing the CPU to different tasks present in the system (including Linux).
  - The RTAI distribution includes three different priority based, pre-emptive real time schedulers:
    - Uni-Processor (UP) scheduler;
    - Multi Uni-Processor (MUP) scheduler;
    - Symmetric Multi-Processor (SMP) scheduler
  - During the installation process, a scheduler is determined based on the hardware configuration of the target machine.

---
RTAI Scheduler
- UP scheduler - For uni-processor platforms.
  - Timer supports either one-shot or periodic scheduling but not both simultaneously.
- SMP scheduler - For multi-processor machines.
  - Timer supports either one-shot or periodic scheduling but not both simultaneously.
  - Tasks can run symmetrically on any or a cluster of CPUs, or be bound to a single CPU.
  - By default all tasks are defined to run on any of the CPUs and are automatically moved between CPUs as the system's processing and load requirements change.

---
RTAI Scheduler
- Multi-Uniprocessor scheduler - For multiprocessor platforms only and supports both one-shot and periodic scheduling simultaneously.
  - The main advantage is the ability to be able to use mixed timers simultaneously, i.e. periodic and one-shot timers.
  - Periodic timers can be based on different periods.
  - Like the SMP schedulers, the MUP can use inter-CPU services related to semaphores, messages and mailboxes.

---
Scheduler Functionality
- The RTAI multitasking scheduler, uses interrupt-driven, priority-based task scheduling.
- The scheduler elects the first highest priority task in a READY state.
  - Priority 0 is the highest priority and 0x3fffFfff the lowest for rtai tasks
  - Linux is given priority 0x7fffFfff.
  - RTAI takes care of Linux activation. When timer handler is running and the next Linux time period is reached a Linux pending interrupt is raised and will be served by the dispatcher.

---
Scheduler Functionality
- All RTAI schedulers incorporate standard RTOS scheduling services like resume, yield, suspend, make periodic, wait until etc.
- The scheduler looks for ready tasks or tasks with expired period.
  - A task may be in the following states : READY, SUSPENDED, DELAYED, SEMAPHORE, SEND, RECEIVE, RPC, RETURN, RUNNING, DELETED
  - On Timer event, the timer handler changes the task state.

---
Scheduler Functionality
- Applications using RTAI schedulers can be timed by three type of hard timers:
  - 8254: Allows one shot and periodic modes
    - Special care is taken in maintaining Linux timing
    - One-Shot mode is provided by Time Stamp Clock (TSC) or Counter2
  - APIC: Allows one shot and periodic modes
    - One-Shot mode is provided Time Stamp Clock (TSC)
  - Real Time Clock (RTC): Allows just periodic mode
    - Periodic ticking at a frequency that is set when configuring RTAI. Frequency can range from 2 to 8192 Hz in power of 2 always

---
RTAI FIFOs
- Fifos allow Linux processes and RTAI tasks to exchange byte-oriented data steams.
  - A fifo is a one way channel therefore a duplex communication needs 2 fifos.
  - From a Linux process point of view the mechanism allows either blocking or non-blocking IO depending on user program.
  - From a task point of view fifo allows non-blocking or asynchronous IO.
  - To perform synchronous reads (and to avoid polling) RTAI makes it possible to attach a user real time handler to a fifo.

---
RTAI FIFOs
- From a software point of view Fifo's are:
  - A Linux device driver for processes
  - System calls for real time tasks
- Fifo's initialization exports procedural functions rtf_create, rtf_create_handler for tasks and installs a device driver used by Linux processes.
  - The driver functions available for Linux processes are seek, read, write, poll, open, release

---
RTAI FIFOs
  - blocking read.
  - rtf_put call.
  - SRQ initialization.
  - wake-up action in queue.
  - wake-up action de-queued at next Linux scheduling

---
RTAI LXRT Module
LXRT is a module that allows to use all the services made available by RTAI and its schedulers in user space, both for soft and hard real time.